## Slide 1: Obstacle Avoiding Car
Day 5

## Slide 2: Today
Basic programming elements
  Conditions
  Functions

## Slide 3: Conditions
Let something happen if some requirements are fulfilled.
For example,

## Slide 4
If this is Aftari time?
Have some food …

## Slide 5: Similarly, in programming
if ( it is raining )
{
// look up, is there water falling on me?
if ( I have an umbrella )
{
OpenUmbrella();
//Opening Umbrella operation
}
}

## Slide 6: Today’s Task
We will make an obstacle avoiding car, and implement conditions in it.

## Slide 7: What it will do?
  Check if there is any hurdle
  Stop if any hurdle appears
  Move forward if there is no hurdle
  Repeat the process

## Slide 8: Let’s have a look at code!
void loop()
{
CheckDistance();
if(distance>15)
{
MoveForward();
}
}

## Slide 9: Now looking inside …
void loop()
{
CheckDistance();
if(distance>15)
{
MoveForward();
}
}
Let us see what’s happening inside the functions!

## Slide 10: Check Distance
void CheckDistance()
{
digitalWrite(trig, LOW);
delayMicroseconds(2);
digitalWrite(trig, HIGH);
delayMicroseconds(10);
digitalWrite(trig, LOW);
duration = pulseIn(echo, HIGH);
inches = duration/74/2;//converts time duration to inches
cm = duration / 29 / 2;//converts time duration to cm
distance = cm;
}

## Slide 11: Move Forward
void MoveForward()
{
digitalWrite(in1, HIGH);
digitalWrite(in2, LOW);
analogWrite(enA, 150);
digitalWrite(in3, HIGH);
digitalWrite(in4, LOW);
analogWrite(enB, 150);
delay(1000);
}

## Slide 12: Next Time
Next time we will add functions to move the car in all directions i.e.
  Forward
  Backward
  Right
  Left