## Slide 1: Obstacle Avoiding Car
Day 5

## Slide 2: Today
Basic programming elements
  Conditions
  Functions

## Slide 3: Conditions
Let something happen if some requirements are fulfilled.
For example,

## Slide 4
If this is Aftari time?
Have some food …

## Slide 5: Similarly, in programming
if ( it is raining )
{
// look up, is there water falling on me?
if ( I have an umbrella )
{
OpenUmbrella();
//Opening Umbrella operation
}
}

## Slide 6: Today’s Task
We will make an obstacle avoiding car, and implement conditions in it.

## Slide 7: What it will do?
  Check if there is any hurdle
  Stop if any hurdle appears
  Move forward if there is no hurdle
  Repeat the process

## Slide 8: Let’s have a look at code!
void loop()
{
CheckDistance();
if(distance>15)
{
MoveForward();
}
}

## Slide 9: Now looking inside …
void loop()
{
CheckDistance();
if(distance>15)
{
MoveForward();
}
}
Let us see what’s happening inside the functions!

## Slide 10: Check Distance
void CheckDistance()
{
digitalWrite(trig, LOW);
delayMicroseconds(2);
digitalWrite(trig, HIGH);
delayMicroseconds(10);
digitalWrite(trig, LOW);
duration = pulseIn(echo, HIGH);
inches = duration/74/2;//converts time duration to inches
cm = duration / 29 / 2;//converts time duration to cm
distance = cm;
}

## Slide 11: Let’s get started!
Now, we will see our code in chunks!
  Check how Ultrasonic sensor works!
  Measure the distance
  Move the Car Forward
  Combine both parts

## Slide 12: Connect the Sensor

## Slide 13: Setup the Sensor
// ultrasonic sensor
const int VCC = 10;
const int trig = 11;
const int echo = 12;
const int GND = 13;

## Slide 14: Understand the Configuration
void setup()
{
pinMode(VCC,OUTPUT);
pinMode(GND,OUTPUT);
digitalWrite(VCC,HIGH);
digitalWrite(GND,LOW);
pinMode(trig,OUTPUT);
pinMode(echo,INPUT);
Serial.begin(9600);
}

## Slide 15: Move Forward
void MoveForward()
{
digitalWrite(in1, HIGH);
digitalWrite(in2, LOW);
analogWrite(enA, 150);
digitalWrite(in3, HIGH);
digitalWrite(in4, LOW);
analogWrite(enB, 150);
delay(1000);
}

## Slide 16: Finally . . .
void loop()
{
CheckDistance();
Serial.println(distance);
if(distance<50)
{
Stop();
}
if(distance>50)
{
MoveForward();
}
}